## Slide 1
INTRODUCTION TO MICROCONTROLLERS

## Slide 2
Definition of a microcontroller
Designed to perform specific tasks in embedded systems
Small, self-contained computer on a single chip
Contains CPU, memory (RAM, Flash), and I/O peripherals
Helps to change the function without changing the electronic circuit

## Slide 3
Historical background
2000s–Present: Dominance of ARM Cortex-M, IoT expansion
1971: 4-bits microcontroller – Intel 4004 used in calculators by a Japanese company named BUSICOM
1980s–90s: Rise of 8051, PIC, and AVR families
1973: 12-bits microcontroller – Toshiba TLCS-12 used in Ford’s cars as engine controller

## Slide 4
Architecture overview
Harvard architecture
Von Neumann architecture
Known as RISC (Reduced Instruction Set Computer)
Known as CISC (Complex Instruction Set Computer)
Newer than Von Neumann
Memory bus and Data bus are separate which allows simultaneous access to data and instructions (Faster)
Shared bus, which can cause the von Neumann bottleneck (a limitation in data throughput)
Simpler design

## Slide 5
Architecture overview
RISC architecture
CISC architecture
Contains a hardwired programming unit
Microcoded (implemented via small programs inside the CPU)
Simple instructions decoding
A single clock cycle for instruction execution
Less usage of memory
Less number of instructions
Fixed size for instructions (32bits-4bytes)
Variable size for instructions (16 to 64 bits for each instruction)
Performance is optimized with a focus on hardware
Performance is optimized, with an emphasis on software
Commonly used in ARC, Alpha, ARC, ARM, AVR, PA-RISC, and SPARC.
Commonly used in System/360, VAX, AMD, and Intel x86 processors.

## Slide 6
Architecture overview

## Slide 7
Some features and capabilities
Low-power and sleep modes
Digital & Analog I/O
Timers, PWM, watchdogs
Communication: UART, I2C, SPI, CAN
Built-in ADC, DAC

## Slide 8
Applications of microcontrollers
Robotics and automation
Home appliances
Automotive
Medical devices
IoT and smart devices

## Slide 9
Popular microcontroller platforms
PIC & AVR: Widely used in legacy systems
Arduino: Easy for beginners, based on AVR/ARM
ESP32/ESP8266: Wi-Fi/Bluetooth enabled
STM32/NXP: Industrial-grade, ARM Cortex-M
Raspberry Pi Pico: Dual-core RP2040 MCU

## Slide 10
Challenges and considerations
Security in connected systems
Limited memory and processing power
Real-time performance requirements
Power management in portable devices

## Slide 11
Software considerations
Number of inputs/outputs (GPIO)
Types of communication protocols needed
Hardware considerations
CPU frequency needed and decide if an external clock is nedded
Mathematical calculations (fixed point, floating point)
Microcontroller architecture
Data size (8-bit, 16-bit or 32-bit) that a CPU can handle at a time
Selecting a microcontroller

## Slide 12
Search for adequate microcontroller
Search for communities and sources of support
Examination of costs
Examination of scalability (for future upgrades)
Examination of development tools
Selecting a microcontroller
Memory considerations
Flash size and RAM size
Special features considerations
Built-in peripherals (PWM, ADC…), Operating voltage …